## Slide 1
External interrupts triggered by:
  INT0 or INT1 pins
  Any of the PCINT23:0 pins
INT0 and INT1 are mapped with the pins PD2 and PD3 on ATMega328P
PD2 and PD3 are mapped with digital pins 2 and 3 (GPIO) on the Arduino Uno board
PCINT23:0 are mapped with ports B, C, and D on the Arduino Uno board
Implies any of the I/O pins on the board can be configured to handle interrupts
These interrupts can be used to wake up the processor from sleep modes
External Interrupts

## Slide 2: External Interrupts
INT0 and INT1 are referred to as ‘External Interrupts’
  Can be triggered by a rising edge, falling edge, logical change, or low level
PCINT23:0 are referred to as ‘Pin Change Interrupts’
External interrupts have a higher priority
External interrupts have their own interrupt vectors
Pin change interrupts share interrupt vectors
  The interrupt handler has to decide which pin the interrupt originated from

## Slide 3: PCICR – Pin Change Interrupt Control Register
Bits 7: 3 – Reserved – always read as 0
Bit 2 – PCIE2 – Pin Change Interrupt Enable 2
Bit 1 – PCIE1 – Pin Change Interrupt Enable 1
Bit 0 – PCIE0 – Pin Change Interrupt Enable 0

## Slide 4: PCICR – Pin Change Interrupt Control Register
If PCIEx is enabled and I bit in SREG is enabled, pin change interrupt x is enabled
PCINT 23:16 corresponds to pin change interrupt 2
PCINT 14:8 corresponds to pin change interrupt 1
PCINT 7:0 corresponds to pin change interrupt 0
The pins are enabled individually from PCMSKx register
Executed from PCIx interrupt vector
Any change in these pins will cause an interrupt

## Slide 5: PCICR – Pin Change Interrupt Control Register
PCINT 23:16 –
  PD7:PD0 on ATMega328P
  Pins D7:D0 (GPIO) on Arduino Uno board
PCINT 14:8 –
  PC6:PC0 on ATMega328P
  PC5:0 – Pins A5:A0 on Arduino Uno board
  PC6 – Reset pin on Arduino Uno Board
PCINT 7:0 –
  PB7:PB0 on ATMega328P
  PB5:0 – Pins D13:D8 on Arduino Uno board
  PB6 and PB7 are not available externally on the Arduino Uno board

## Slide 6: PCIFR – Pin Change Interrupt Flag Register
Bits 7:3 – Reserved – Always read as 0
Bit 2 – PCIF2 – Pin Change Interrupt Flag 2
Bit 1 – PCIF1 – Pin Change Interrupt Flag 1
Bit 0 – PCIF0 – Pin Change Interrupt Flag 0

## Slide 7: PCIFR – Pin Change Interrupt Flag Register
Any logic change on PCINT23:0 triggers an interrupt request: PCIFx set
If I bit in SREG and PCIEx on PCICR are set, MCU will go to the corresponding interrupt vector
Flag is cleared when:
  Interrupt routine is executed
  A logical 1 is written

## Slide 8: PCMSK2 – Pin Change Mask Register 2
Bits 7:0 – PCINT23:16 – Pin Change Enable Mask 23:16
Each bit selects whether the pin change interrupt is enabled on the corresponding I/O pin
If any bit from PCINT23:16 is set and the PCIE2 bit on PCICR is set, pin change interrupt is enabled on the corresponding I/O pin
If PCINT23:16 is cleared, the pin change interrupt on the corresponding I/O pin is disabled

## Slide 9: PCMSK1 – Pin Change Mask Register 1
Bit 7 – Reserved – Always read as 0
Bits 6:0 – PCINT14:8 – Pin Change Enable Mask 14:8
Each bit selects whether the pin change interrupt is enabled on the corresponding I/O pin
If any bit from PCINT14:8 is set and the PCIE1 bit on PCICR is set, pin change interrupt is enabled on the corresponding I/O pin
If PCINT14:8 is cleared, the pin change interrupt on the corresponding I/O pin is disabled

## Slide 10: PCMSK0 – Pin Change Mask Register 0
Bits 7:0 – PCINT7:0 – Pin Change Enable Mask 7:0
Each bit selects whether the pin change interrupt is enabled on the corresponding I/O pin
If any bit from PCINT7:0 is set and the PCIE0 bit on PCICR is set, pin change interrupt is enabled on the corresponding I/O pin
If PCINT7:0 is cleared, the pin change interrupt on the corresponding I/O pin is disabled